## Slide 1: market rules Overview: CAISO
April 2025

## Slide 2: Overview of CAISO market value streams
 | Value Stream | Front-the-meter DER | Behind-the-meter DER | Bid Components (for each trading hour) | Settlements (quantity & price)
1 | Time-Of-Use Energy | No | Yes | N/A | Energy, at retailer’s TOU price
2.1 | Demand Charge: coincident (peak) | No | Yes | N/A | Peak demand, at retailer’s Coincident DC price
2.2 | Demand Charge: non-coincident (off-peak) | No | Yes | N/A | Off-peak demand, at retailer’s Non-coincident DC price
3 | Demand Response: DSGS or ELRP? | No | Yes | ? | ?
4 | Carbon Market: LCFS | ? | Yes, only for EVSE | N/A | Energy, at LCFS price
5 | Wholesale Energy: Day-Ahead (DAM) and Real-Time (RTM) | Yes | Yes, with limitations: Sell if price > NBT threshold No net export of facility + DER Buy if price < 0 | Bid curve (MW vs price) | DA energy award at DA LMP RT energy award at RT LMP
6.1 | AS: Regulation Up | Yes | No | Capacity Price ($/MW) Ramp Rate (MW/minute) Mileage price ($/MW – default to 0) | DA / RT Capacity award at DA / RT ASMP Dispatched energy at RT LMP Mileage at DA and/or RT mileage price
6.2 | AS: Regulation Down | Yes | No | Capacity Price ($/MW) Ramp Rate (MW/minute) Mileage price ($/MW – default to 0) | DA / RT Capacity award at DA / RT ASMP Dispatched energy at RT LMP Mileage at DA and/or RT mileage price
6.3 | AS: Spinning reserve | Yes | Yes | Capacity Price ($/MW) | DA / RT Capacity award at DA / RT ASMP Dispatched energy at RT LMP
6.4 | AS: Non-spinning Reserve | Yes | Yes | Capacity Price ($/MW) | DA / RT Capacity award at DA / RT ASMP Dispatched energy at RT LMP
7 | Flexible Ramping Product (FRP) | Yes | Yes through flexible resource adequacy | Residual Unit Commitment (RUC) capacity? | DA bid?? Flexible Ramp Forecasted Movement capacity Uncertainty Ramp-up capacity Uncertainty Ram-down capacity Dispatched energy at RT LMP

## Slide 3: Market Timeline overview
Source: CAISO: Overview of Market Processes, CAISO, 2022
Day-Ahead Market (DAM)
Real-Time Market (RTM)
Post market activities
RTM settlement
HASP -> advisory dispatches/awards. Dispatch only long inertia resources
D-7days
D-1 at 10:00
D-1 at 13:00
T-75min
DAM bids submission
DAM settlement
Market power mitigation (MPM) checks and mitigates bids
Integrated forward market (IFM) settles the awards for each trading hour
Takeaways
DAM bids and awards are for each trading hour
RTM bids are for each trading hour, but:
  Capacity awards (and some energy awards for generators who need to shut-down/start-up/transition slowly) are for each 15 minutes interval of the trading hour
  Energy is dispatched every 5 minutes
Send metering information
Final settlements
DAM open
DAM settles
RTM open
RTM settles
Start of trading hour (T)
End of trading hour
T-15
T-5
FMM -> settles awards for next 15min of the trading hour. Dispatch only resources that need to start up or shut down
RTD -> dispatch instructions sent based on awards

## Slide 4: Ancillary services Specific rules
Regulation
For small mismatch btw supply and demand, small freq. deviations
  Regulation up
  Regulation down
Operating Reserve
To make up for large generation deficiencies (e.g., loss of a whole generation unit)
  Spinning Reserve
  Load already synchronized to the grid
  Non-spinning Reserve
  Load not synchronized (offline) that would have to start and ramp up
Requirements
For Day-Ahead Market (DAM) award:
Be able to sustain awarded capacity for 60 minutes
Settlements
Capacity payment from market award
Energy payment from energy dispatched (area under AGC curve)
[Optional] Mileage payment (for accurate AGC signal variation tracking)
Capacity payment from market award
Energy payment from energy dispatched (area under blue)
Requirements are enforced by the market, make sure we put them as SOC constraints
Source: Tariff section 8.4.3, Tariff appendix K
For Real-Time Market (RTM) award:
Be able to sustain awarded capacity for 30 minutes
Ramp up to awarded capacity in 10 minutes max
Be able to sustain awarded capacity for 30 minutes
+
Signal tracking accuracy requirement

## Slide 5: Ancillary services Example of dispatch for one trading hour
Chart: kW
| 0 | 6.9444444444444447E-4 | 1.38888888888889E-3 | 2.0833333333333298E-3 | 2.7777777777777801E-3 | 3.4722222222222199E-3 | 4.1666666666666701E-3 | 4.8611111111111103E-3 | 5.5555555555555601E-3 | 6.2500000000000003E-3 | 6.9444444444444397E-3 | 7.6388888888888904E-3 | 8.3333333333333297E-3 | 9.0277777777777804E-3 | 9.7222222222222206E-3 | 1.0416666666666701E-2 | 1.1111111111111099E-2 | 1.18055555555556E-2 | 1.2500000000000001E-2 | 1.3194444444444399E-2 | 1.38888888888889E-2 | 1.4583333333333301E-2 | 1.52777777777778E-2 | 1.59722222222222E-2 | 1.6666666666666701E-2 | 1.7361111111111101E-2 | 1.8055555555555599E-2 | 1.8749999999999999E-2 | 1.94444444444444E-2 | 2.0138888888888901E-2 | 2.0833333333333301E-2 | 2.1527777777777798E-2 | 2.2222222222222199E-2 | 2.29166666666667E-2 | 2.36111111111111E-2 | 2.4305555555555601E-2 | 2.5000000000000001E-2 | 2.5694444444444402E-2 | 2.6388888888888899E-2 | 2.70833333333333E-2 | 2.7777777777777801E-2 | 2.8472222222222201E-2 | 2.9166666666666698E-2 | 2.9861111111111099E-2 | 3.05555555555556E-2 | 3.125E-2 | 3.19444444444444E-2 | 3.2638888888888898E-2 | 3.3333333333333298E-2 | 3.4027777777777803E-2 | 3.4722222222222203E-2 | 3.54166666666667E-2 | 3.6111111111111101E-2 | 3.6805555555555598E-2 | 3.7499999999999999E-2 | 3.8194444444444399E-2 | 3.8888888888888903E-2 | 3.9583333333333297E-2 | 4.0277777777777801E-2 | 4.0972222222222202E-2
AGC signal | 6 | 5 | 3 | 2 | 1 | 4 | 8 | 9 | 6 | 5 | 8 | 10 | 2 | 3 | 6 | 2 | 5 | 1 | 4 | 5 | 8 | 12 | 5 | 8 | 6 | 3 | 2 | 0 | 1 | 4 | 0 | 8 | 0 | 4 | 7 | 14 | 14 | 6 | 3 | 6 | 4 | 5 | 7 | 7 | 9 | 6 | 5 | 8 | 11 | 10 | 6 | 5 | 9 | 1 | 0 | 2 | 5 | 6 | 3 | 5
Award | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 14 | 14 | 14 | 14 | 14 | 14 | 14 | 14 | 14 | 14 | 14 | 14 | 14 | 14 | 14 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11
Chart: kW
| 0 | 6.9444444444444447E-4 | 1.38888888888889E-3 | 2.0833333333333298E-3 | 2.7777777777777801E-3 | 3.4722222222222199E-3 | 4.1666666666666701E-3 | 4.8611111111111103E-3 | 5.5555555555555601E-3 | 6.2500000000000003E-3 | 6.9444444444444397E-3 | 7.6388888888888904E-3 | 8.3333333333333297E-3 | 9.0277777777777804E-3 | 9.7222222222222206E-3 | 1.0416666666666701E-2 | 1.1111111111111099E-2 | 1.18055555555556E-2 | 1.2500000000000001E-2 | 1.3194444444444399E-2 | 1.38888888888889E-2 | 1.4583333333333301E-2 | 1.52777777777778E-2 | 1.59722222222222E-2 | 1.6666666666666701E-2 | 1.7361111111111101E-2 | 1.8055555555555599E-2 | 1.8749999999999999E-2 | 1.94444444444444E-2 | 2.0138888888888901E-2 | 2.0833333333333301E-2 | 2.1527777777777798E-2 | 2.2222222222222199E-2 | 2.29166666666667E-2 | 2.36111111111111E-2 | 2.4305555555555601E-2 | 2.5000000000000001E-2 | 2.5694444444444402E-2 | 2.6388888888888899E-2 | 2.70833333333333E-2 | 2.7777777777777801E-2 | 2.8472222222222201E-2 | 2.9166666666666698E-2 | 2.9861111111111099E-2 | 3.05555555555556E-2 | 3.125E-2 | 3.19444444444444E-2 | 3.2638888888888898E-2 | 3.3333333333333298E-2 | 3.4027777777777803E-2 | 3.4722222222222203E-2 | 3.54166666666667E-2 | 3.6111111111111101E-2 | 3.6805555555555598E-2 | 3.7499999999999999E-2 | 3.8194444444444399E-2 | 3.8888888888888903E-2 | 3.9583333333333297E-2 | 4.0277777777777801E-2 | 4.0972222222222202E-2
AGC signal | 2 | 2 | 2 | 2 | 2 | 4 | 4 | 4 | 4 | 4 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 8 | 10 | 12 | 12 | 12 | 11 | 11 | 11 | 11 | 11 | 10 | 10 | 10 | 10 | 10 | 12 | 12 | 12 | 12 | 12 | 10 | 8 | 6 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 2 | 0 | 0 | 0 | 0
Award | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 14 | 14 | 14 | 14 | 14 | 14 | 14 | 14 | 14 | 14 | 14 | 14 | 14 | 14 | 14 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11
Maximum Ramp-up/down rates respected
AGC signal can change every 4 seconds
Dispatch order can change every 5 minutes
Spinning or Non-Spinning reserve dispatch example
Regulation up dispatch example
DAM + RTM Award
Dispatch Signal
Our dispatch simplification
Chart: kW
| 0 | 6.9444444444444447E-4 | 1.38888888888889E-3 | 2.0833333333333298E-3 | 2.7777777777777801E-3 | 3.4722222222222199E-3 | 4.1666666666666701E-3 | 4.8611111111111103E-3 | 5.5555555555555601E-3 | 6.2500000000000003E-3 | 6.9444444444444397E-3 | 7.6388888888888904E-3 | 8.3333333333333297E-3 | 9.0277777777777804E-3 | 9.7222222222222206E-3 | 1.0416666666666701E-2 | 1.1111111111111099E-2 | 1.18055555555556E-2 | 1.2500000000000001E-2 | 1.3194444444444399E-2 | 1.38888888888889E-2 | 1.4583333333333301E-2 | 1.52777777777778E-2 | 1.59722222222222E-2 | 1.6666666666666701E-2 | 1.7361111111111101E-2 | 1.8055555555555599E-2 | 1.8749999999999999E-2 | 1.94444444444444E-2 | 2.0138888888888901E-2 | 2.0833333333333301E-2 | 2.1527777777777798E-2 | 2.2222222222222199E-2 | 2.29166666666667E-2 | 2.36111111111111E-2 | 2.4305555555555601E-2 | 2.5000000000000001E-2 | 2.5694444444444402E-2 | 2.6388888888888899E-2 | 2.70833333333333E-2 | 2.7777777777777801E-2 | 2.8472222222222201E-2 | 2.9166666666666698E-2 | 2.9861111111111099E-2 | 3.05555555555556E-2 | 3.125E-2 | 3.19444444444444E-2 | 3.2638888888888898E-2 | 3.3333333333333298E-2 | 3.4027777777777803E-2 | 3.4722222222222203E-2 | 3.54166666666667E-2 | 3.6111111111111101E-2 | 3.6805555555555598E-2 | 3.7499999999999999E-2 | 3.8194444444444399E-2 | 3.8888888888888903E-2 | 3.9583333333333297E-2 | 4.0277777777777801E-2 | 4.0972222222222202E-2
AGC signal | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4
Award | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 14 | 14 | 14 | 14 | 14 | 14 | 14 | 14 | 14 | 14 | 14 | 14 | 14 | 14 | 14 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11 | 11
One dispatch order every 15 minutes (as a call rate = % of award)

## Slide 6: Ancillary services overview of prices in January 2025
Service | Mean DAM price in Jan. 2025 ($/MW) | Mean RTM price in Jan. 2025 ($/MW)
Regulation Up | 1.69 | 1.16
Mileage Up | 0.00016 | 0.00058
Regulation Down | 5.62 | 3.32
Mileage Down | 0.0017 | 0.0049
Non-spinning reserve | 0.46 | 0.057
Spinning reserve | 0.49 | 0.06
Regulation prices >> operating reserve prices
Day ahead prices > Real-time prices
Source: OASIS

## Slide 7: BTM/DER Specific rules & Baseline calculation
For behind-the-meter DERs, all capacity and energy bids in the wholesale market are curtailment or oversupply compared to the baseline
There are different baseline calculation methods for building loads, BTM generation, BTM storage, and EVSEs
Source: BPM for demand response; FERC 2222 CAISO Presentation

## Slide 8: Use Cases
Only bill management
Bill management + DR program
Bill management + Wholesale market + AS (Operating reserve only)
Everything
[Optional] BTM DERs + FTM battery

## Slide 9: Example of equations
We shouldn’t allow to buy electricity from the retailer while simultaneously selling the same amount to the wholesale market, because that is “virual” energy, that never actually flows on the electric network and in the battery.
Basically, either we charge (all Ps are greater or equal to 0) or we discharge (all Ps are less or equal to 0)