## Slide 1
Replace the big-M penalty with CAISO-aligned settlement logic
DA energy is fixed; RT settles deviations; unavailable AS loses capacity payment
UPSCALeDEV | Market settlement update

## Slide 2
2
The old penalty was a tracking device, not a market settlement
OLD M · |λRT| · |DA deviation|
• Arbitrary scale
• Poor economic interpretation
• Can worsen numerical conditioning
REVISED λDA·pDA + λRT·pRT
• pDA is a fixed RT parameter
• pRT is incremental buy-back/sell-back
• Physical capability uses pDA + pRT
Problem
The previous objective multiplied absolute DA deviations by |RT LMP| and M = 100,000.
It behaved almost like a hard constraint, omitted Δt, and treated energy and four AS products identically.
Sources: CAISO Settlements Validation, CC 6011/6460/6470; CAISO BPM for Settlements and Billing.

## Slide 3
3
CAISO separates the DA award, RT energy deviation, and AS availability
DAY AHEAD
REAL TIME
SETTLEMENT
Update
RT buys back or sells the energy deviation; incremental AS clears in RT.
Award
DA energy and AS capacity clear at DA prices.
Account
Energy deviation settles at RT LMP. Unavailable AS capacity receives no pay.
Sources: CAISO AS No Pay briefing (2021); CAISO Ancillary Services Forced Buy-Back initiative.

## Slide 4
4
Implemented settlement mode preserves feasibility without inventing a penalty
Energy
Fix pDA = pDA,ref. Optimize pRT as the incremental imbalance position.
Physical limit
Apply headroom constraints to the net position pDA + pRT, not to each leg separately.
Ancillary services
Retained DA AS ≤ DA award. Any reduction loses the corresponding DA capacity revenue.
Verification
Rolling + perfect + full passed a 96-step sample: no NaNs and exact EV energy closure.
Model scope: simplified CAISO-aligned settlement abstraction; product-specific non-compliance adders remain future work.